## Slide 1: MULTI PURPOSE SECURITY ALARM
BY:
Hamza Ali 15CS19
Rohit Kumar 15CS21
Saad 15CS15
Ahmed Jan 15CS13
Muhammad Jan 15CS11

## Slide 2: INTRODUCTION:
During our journey through train and bus, we carry many important things at lift our and all the time we have fear that someone might lift our luggage or with in home we many precious things which have to be kept safe from outsiders.
So to protect our materials we normally lock our things through old ways by the help of chain and locks. But after all such locks we still have fear that someone may slash the chain or lock and take away our precious material.

## Slide 3
To over come with this fear here is an easy circuit based on NAND gates in the circuit.

## Slide 4: Circuit Components
IC = CD4011
Resisto r = 1K ohm and 4.7 k ohm
Capacitor = 1micro F
Diode
Transistor
Buzzer

## Slide 5: Function of security Alarm
Function of this circuit is very simple and easy output is based on voltage of pin 5.At the time when power supply is attached to the circuit of pin 5. voltage is at zero as the loop is unbroken. Hence at pin 4 , voltage is high which is coupled with pin1 and pin2 which is also at high state. As you know from the truth table of NAND gate when both the inputs are at high state then the output is at the pin 3 of gate1.We get
low which is once more attached to pin 12 as well as 13 moving them also
To the low which in turns makes the pin11 to switch at high switching pin 8 as welll as pin 9 also at high and low voltage at pin 10 due to this transistor linkeed to the via a risistor will not boost the base of it and the alarm will not receive by us. this implies that our stuff is secure.

## Slide 6
Now suppose some one attemt to tke your stuffs then the loop attached to it broken down . At the time loop brokedown , pin 5 as well as 6 shift to high and just opposite work will take place which we have explained above due to pin 10 reaches to high state and transistor begain its conduction an alaram will received by us and alaram will not be stop till the time we once interact again with the loop.